## Slide 1: Attn + metrics + thesis outline
YYYY.MM.DD
Yi Wang
Multi-task cGAN for 3D Building Vectorization

## Slide 2
Outline
Network improvement
Evaluation metrics
Thesis outline
Questions
Next Steps

## Slide 3
Network improvement
Self-attention module:
[1] Woo, Sanghyun, et al. "Cbam: Convolutional block attention module." Proceedings of the European conference on computer vision (ECCV). 2018.

## Slide 4
Network improvement
Self-attention module:
DSM: LSGAN + L1 + SN; fine tuning + network interpolation
Edge/Corner: Cross Entropy
dsm
ortho
Refined DSM
D
Fake or Real?
Refined DSM
ortho
Edge/corner
resnet50
CBAM

## Slide 5
Evaluation metrics
DSM refinement (validation area)
Edge detection  3D model (sample area)
 | RMSE (m) | MAE (m) | NMAD (m)
Coupled-cGAN (200 epoch) | 4.07 | 1.85 | 0.99
Interp-cGAN (100pre+50) | 4.02 | 1.73 | 0.93
Attn-cGAN (100 epoch) | 3.86 | 1.67 | 0.91
 | Footprints |  | nDSM Height (m) |  |  | Roof orientation ()
 | accuracy | IoU | RMSE | MAE | NMAD | 
Results | 0.89 | 0.61 | 2.2 | 0.85 | 0.51 | 9.31
 | Footprints |  | nDSM Height (m) |  |  | 
 | accuracy | IoU | RMSE | MAE | NMAD | 
Results | 0.89 | 0.61 | 2.2 | 0.85 | 0.51 | 9.31

## Slide 6
Thesis outline
Title: Machine-learned 3D Building Vectorization from Satellite Imagery
Abstract:
1. Introduction:
We propose a machine-learning based approach for automatic 3D building reconstruction and vectorization.
Taking single-channel photogrammetric DSM and pan-chromatic (PAN) image as input, we first refine the
DSM shapes with a conditional generative adversarial neural network (GAN). The refined DSM combined with
PAN image are then used to detect roof edges and corners, which are later vectorized to parameterized polygons.
Finally, we add height information from refined DSM to obtain full 3D building models.
Motivation
Relative work
  3D reconstruction (LOD1)
  3D reconstruction (LOD2-like)
  3D reconstruction (LOD2)
  CNN & GAN
  Edge detection & regularization
  vectorization
Our work (highlights)
  DSM refinement
  Edge/corner detection
  vectorization

## Slide 7
Thesis outline
2. Methodology
  2.1 DSM refinement
  2.2 Edge/corner detection
  2.3 3D building model
    Corner: non-maximum suppression
    Edge: corner connectivity
    2D polygon: closed edges
    3D model: roof + wall + ground
Network structure + Losses

## Slide 8
Thesis outline
3. Experiments
  3.1 study area and dataset
  3.2 network implementation details
  3.3 results and evaluation
    3.3.1 result figures (DSM + Edge + 3D model)
    3.3.2 Evaluation DSM
    3.3.3 Evaluation 3D model
      Footprints
      nDSM
      Roof orientation
    (3.3.4 compared to another approach?)

## Slide 9
Thesis outline
4. Conclusion
Summary of our work, discussion, future work
5. Acknowledgement
6. References
7. List of figures
8. List of tables
9. Appendix

## Slide 10
Next steps
Contents here